## Slide 1: Casing selection strategies for SCORE
Lucas Pereira de Gouveia
Universidade Federal de Alagoas

## Slide 2: SCORE project
SCORE projects are imported by means of a json file
All well configuration data are converted in a SCORE project object
CasingDesign is an object type that needs:
  one casing string from a SCORE project
  one load scenario object
CasingDesign results provide:
  load profiles
  safety factor profiles
  failure probabilities profiles

## Slide 3: SCORE tubulars catalog
It is a json file without prices of tubulars (pipes and connections)
For casing selection we insert hypothetical prices in the json file for each tubular

## Slide 4: Hypothetical prices – Data fit
Get one source of price data, fit data and then extrapolate for other tubulars sizes
In this example we use Roque, Maidla e Wagner (1996).
  64 tubes with 7” OD
  27 tubes with 9 5/8” OD
We assume that the price variates according to OD and burst, collapse and axial strengths.
The result for a linear function approach did not perform good. This strategy may need more data to perform better.

## Slide 5: Hypothetical prices – Adapting data from Roque, Maidla e Wagner (1996)
64 tubes with 7” OD
27 tubes with 9 5/8” OD
Some tubes have the same OD, weight and grade, but different strength properties, we believe this
The connection performance reduces the strength of tubulars
  In this case we are calculating with Score-lib the tube strengths properties and choosing the one that matches